## Slide 1
Medieval Style Trebuchet: Assembly Instructions

## Slide 2: Step 1: Place ground plate

## Slide 3: Step 2: Insert Vertical Upright

## Slide 4
Step 3: Insert A-frame pieces

## Slide 5
Step 4: Insert 2x
5*17mm pegs

## Slide 6
Step 5: Repeat process for other upright
then
Place assembly to side to build throwing arm

## Slide 7
Step 6: Assemble throwing arm as shown using
4x
6*23mm pegs

## Slide 8
Step 7: Insert ratchet mechanism in slot shown. Use 1.75mm filament offcut to secure pivot point

## Slide 9
Step 8: Secure Counterweight to throw arm assembly using 2x
6*16mm pegs
Washers should be placed between counterweight and throw arm assembly to allow free rotation of counterweight

## Slide 10
Step 9:
Place throw arm assembly on base assembly Place weights (coins, screws, lead shot etc) in empty counterweight ≥ 200g
(The more weight added the better the trebuchet will work)
~200g

## Slide 11
Step 10:
Tie string to boulder using any method. Create loop in free end and tie slip knot as shown, such that the length of the finished string, including loop is between approximately 13, and 23cm String length can be adjusted by moving position of slip knot

## Slide 12
Step 11:
Place free loop of string over the adjustable angle throwing pin (A)
Set release angle using ratchet mechanism B
Place boulder in throwing position (as shown C)
Aim trebuchet at target
Pull back to full extent available, and release to launch boulder
A
C
Warning! Use Trebuchet Responsibly
- Do not launch at pets!
- Not suitable for conducting Siege warfare
B